Non-Assessed 2FCMb Practice in Generating a Weibull Plot
You are given data (see below) for a ceramic material, determined in 3-point flexural
strength tests conducted at a strain rate of 1 x 10-3 s-1 .

You are required to:

(i) Find out what are the sample standard deviation and coefficient of variation of a
data set are defined as, and how to calculate these parameters.
s.d. = sqrt{sum{(x-bar{x})^2} over {n-1}}	CV = {s.d.} over {mean} = σ over bar{x}

(ii) Calculate the mean flexural strength, together with the sample standard deviation
and coefficient of variation for the flexural strength data.
σ= 118.7MPa;	x̄ = 301.6 MPa	CV = 0.393

(iii) Draw a graph of survival probability P s against flexural strength, s. Use the mean
rank Ps (survival probability) estimator.

(iv) Draw the corresponding Weibull graph for the material, using the mean rank P s
(survival probability) estimator, and tabulating all the relevant numerical data.

(v) Using the data from (iv), determine the Weibull modulus, m value for the material
graphically using least-squares linear regression method to generate the “best-fit”
trend-line, giving the regression equation and correlation coefficient R.

Given the number of data, it is recommended that while you check your calculations
manually, you use a spreadsheet program such as Excel to tabulate the data, do the
calculations, and plot the graphs.

The 3-Point Flexural Strength Data for a Ceramic (MPa) is omitted from here.